## Slide 1: FP Instructions in MIPS
FP hardware is coprocessor 1
  Adjunct processor that extends the ISA
  Also called FPU co-processor

## Slide 2: FP Instructions in MIPS
Separate FP registers
  32 single-precision: $f0, $f1, … $f31
  Paired for double-precision: $f0/$f1, $f2/$f3,
FP instructions operate only on FP registers
  Programs generally don’t do integer ops on FP data, or vice versa
  More registers with minimal code-size impact
Separate FP instructions for single/double precision
  Single precision: (.s extension)
  Double precision: (.d extension)

## Slide 3: FP Arithmetic Instructions

## Slide 4: FP Load/Store Instructions
Separate floating point load/store instructions
lwc1: load word coprocessor 1
ldc1: load double coprocessor 1
swc1: store word coprocessor 1
sdc1: store double coprocessor 1

## Slide 5: FP Load/Store pseudo instructions
l.s = lwc1 (load FP single)
s.s = swc1 (store FP single)
l.d = ldc1 (load FP double)
s.d = sdc1 (store FP double)

## Slide 6: Loading immediate value
load immediate pseudoinstruction.
  li.s fd, value # load register $fd with val
Example:
li.s $f1,1.0 # $f1 = constant 1.0
li.s $f2,2.0 # $f2 = constant 2.0
li.s $f10,1.0e-5 # $f10 = 0.00001

## Slide 7: FP Data Movement Instructions
Moving data between general purpose and FP registers
  mfc1: move from coprocessor 1 (to general purpose register)
  mtc1: move to coprocessor 1 (from general purpose register)
Moving data between FP registers
  mov.s: move single precision float
  mov.d: move double precision float = even/odd pair of registers

## Slide 8: FP Data Movement Instructions

## Slide 9: FP Convert Instructions
Convert instruction: cvt.x.y
Convert to destination format x from source format y
Supported formats
  Single precision float = .s (single precision float in FP register)
  Double precision float = .d (double float in even-odd FP register)
  Signed integer word = .w (signed integer in FP register)

## Slide 10: FP Convert Instructions

## Slide 11: FP Compare and Branch Instructions
FP unit (co-processor 1) has a condition flag
  Set to 0 (false) or 1 (true) by any comparison instruction
Three comparisons:
  equal, less than, less than or equal
Two branch instructions based on the condition flag

## Slide 12: FP Compare and Branch Instructions

## Slide 13: Reading and printing single and double values

## Slide 14: Datatypes

## Slide 15: Floating-Point Data Declarations
The above declarations are used to define floating-point variables "pi" to a 32-bit floating-point value initialized to 3.14159 and "tao" to a 64-bit floating-point values initialized them to 6.28318

## Slide 16: Example:1 Area of a Circle

## Slide 17: Example 2: °F to °C
C code:
float f2c (float fahr) { return ((5.0/9.0)*(fahr - 32.0)); }
.data
const5: .float 5.0
const9: .float 9.0
const32: .float 32.0
constf: .float 50.0
.text
.globl main
main:
l.s $f16, const5
l.s $f18, const9
div.s $f16, $f16, $f18
l.s $f12, constf
l.s $f18, const32
sub.s $f18, $f12, $f18
mul.s $f12, $f16, $f18
li $v0, 2
syscall
li $v0, 10
syscall

## Slide 18: Example 3: ax^2 + bx + c for user-input x
.data
a: .float 1.0
bb: .float 2.0
c: .float 3.0
msg: .asciiz "Enter x: "
blank: .asciiz " "
newl: .asciiz "\n"
.text
.globl main

## Slide 19
main: # read input
la $a0,msg # prompt user for x
li $v0,4 # print string
syscall
li $v0,6 # read single
syscall # $f0 <-- x
# evaluate the quadratic
l.s $f2,a # sum = a
mul.s $f2,$f2,$f0 # sum = ax
l.s $f4,bb # get b
add.s $f2,$f2,$f4 # sum = ax + b
mul.s $f2,$f2,$f0 # sum = (ax+b)x = ax^2 +bx
l.s $f4,c # get c
add.s $f2,$f2,$f4 # sum = ax^2 + bx + c

## Slide 20
# print the result
mov.s $f12,$f2 # $f12 = argument
li $v0,2 # print single
syscall
la $a0,newl # new line
li $v0,4 # print string
syscall
li $v0,10 # code 10 == exit
syscall # Return to OS.