## Slide 1: Principle of Locality
Programs
  want unlimited amounts of fast memory
Program behavior
  access a small proportion of its address space at any time
  exhibits spatial and temporal locality
  Temporal locality (locality in time)
  Spatial locality (locality in space)
§5.1 Introduction

## Slide 2: Principle of Locality
Temporal locality
  Items accessed recently are likely to be accessed again soon
  e.g., instructions in a loop
Spatial locality
  Items near those accessed recently are likely to be accessed soon
  E.g., sequential instruction access, accessing array data
§5.1 Introduction

## Slide 3: Memory hierarchy
Consists of multiple levels of memory with different speeds, sizes & costs
The faster memory is close to the processor and the slower, less expensive memory is below it
Take advantage of principle of locality
§5.1 Introduction

## Slide 4: Memory hierarchy
§5.1 Introduction

## Slide 5: Memory hierarchy
§5.1 Introduction

## Slide 6: Technology for memory hierarchy
Static RAM (SRAM)
  0.5ns – 2.5ns, $2000 – $5000 per GB
  Cache memory
Dynamic RAM (DRAM)
  50ns – 70ns, $20 – $75 per GB
  Main memory
Magnetic disk
  5ms – 20ms, $0.20 – $2 per GB
§5.2 Memory Technologies

## Slide 7: Data in memory hierarchy
The data is hierarchical
Data is copied between only two adjacent levels at a time
Store everything on disk
Copy recently accessed (and nearby) items from disk to smaller Main memory
Copy more recently accessed (and nearby) items from Main memory to Cache memory
§5.1 Introduction

## Slide 8: Memory Hierarchy - HIT
Block (aka line): unit of copying
  Consists of multiple words
Hit
  If data requested by processor is present in upper level
Hit rate or Hit ratio
  Fraction of memory accesses found in the upper level
  Hit rate = hits/accesses
Hit time
  The time to access the upper level of the memory hierarchy which includes the time needed to determine whether the access is a hit or a miss
§5.1 Introduction

## Slide 9: Memory Hierarchy - MISS
Miss
  If data requested is absent in upper level
Miss rate or ratio
  Fraction of memory accesses not found in the upper level
  Miss rate = misses/accesses
  Miss rate = 1 – hit ratio
Miss penalty:
  The time to replace a block in the upper level with the corresponding block from the lower level, plus the time to deliver this block to the processor
§5.1 Introduction

## Slide 10: Cache Memory
Small amount of fast memory
Sits between main memory and CPU
May be located on CPU chip

## Slide 11: Cache operation – overview
CPU requests contents of memory location
Check cache for this data
If present, get from cache (fast)
If not present, read required block from main memory to cache
Then deliver from cache to CPU
Cache includes tags to identify which block of main memory is in each cache slot

## Slide 12: Cache operation - Flowchart
RA – Read address

## Slide 13: Average memory access time
Suppose that a processor has a cache and a main memory. The access time of cache is 0.01 ms; The access time of main memory is 0.1 ms.
Suppose 95% of the memory accesses are found in the cache. Find the average memory access time

## Slide 14: Average memory access time
Average memory access time
  Tavg = h*Tc +(1-h)*M
  h = hit rate
  (1-h) = miss rate
  Tc = time to access information from cache
  M = miss penalty
  = (0.95)(0.01 ms) + (0.05)(0.01 ms + 0.1 ms)
  = 0.0095 + 0.0055 = 0.015 ms

## Slide 15: Main memory
With n-bit address there can be 2n addressable words
Main memory (MM) is considered to consist of a number of fixed length blocks of K words each
Total number of blocks in MM M = 2n/K
§5.3 The Basics of Caches

## Slide 16: Cache memory
The cache consists of m blocks, called lines
Size of a cache line = Size of a main memory block
Each line contains
  K words
  Tag of a few bits
  Control bits
    Ex. Modified/Not modified
    Valid/Invalid
§5.3 The Basics of Caches

## Slide 17: Mapping blocks to lines
The number of lines in cache is less than the number of main memory blocks (m <<M)
At any time, some subset of the blocks of memory resides in lines in the cache
Because there are more blocks than lines, an individual line cannot be uniquely and permanently dedicated to a particular block
Each line has a tag
  Tag identifies which particular block is currently being stored in a line

## Slide 18: Mapping blocks to lines
Because there are fewer cache lines than main memory blocks, an algorithm is needed for mapping main memory blocks into cache lines
Further, a means is needed for determining which main memory block currently occupies a cache line
The choice of the mapping function dictates how the cache is organized
Three techniques can be used: direct, associative, and set associative

## Slide 19: Main memory - Example
Main memory address has two fields
  s bits specify one of the 2s blocks of main memory
  w bits identify a unique word or byte within a block of main memory
  block address + word offset
Main memory of 16MB
Address bits : 24 bits
Main memory block of 4 bytes
  No. of MM blocks = MM size/block size
  No. of MM blocks = 16MB/ 4B = 4MB = 222
  No. of bits to address 4 MB MM blocks
  = log (222) = 22 bits
  No. of bits to address 4 bytes = log(4) = 2 bits
24 bit address = 22 bit block address and 2 bit word offset

## Slide 20: Cache memory - Example
Cache of 64KB
Cache block of 4 bytes
  No. of cache lines = Cache size/block size
  No. of cache lines = 64KB/ 4B = 16 KB = 214
  No. of bits to address 14 KB cache lines
  = log (214) = 14 bits
  No. of bits to address 4 bytes = log(4) = 2 bits

## Slide 21: Direct Mapped Cache
Simplest technique
Each block of main memory maps into only one possible cache line
The mapping is expressed as
i = j modulo m
i cache line number
j main memory block number
m number of lines in the cache

## Slide 22: Direct Mapping from Cache to Main Memory

## Slide 23: Direct Mapping Cache Line Table
Cache line | Main Memory blocks held
0 | 0, m, 2m, 3m…2s-m
1 | 1,m+1, 2m+1…2s-m+1
… | 
m-1 | m-1, 2m-1,3m-1…2s-1

## Slide 24: Direct Mapping Address
For purposes of cache access, each main memory address can be viewed as consisting of three fields
  Line offset
    Identifies a unique word or byte within a line of cache memory
    The least significant w bits
  Line number
    Specify one of the m=2r blocks of main memory
    The next most significant r bits
  Tag
    Distinguish a block from other blocks that can fit into a cache line
    The most significant portion s – r bits

## Slide 25: Direct Mapping Address
Address length = (s + w) bits
Number of addressable units = 2s+w words or bytes
Block size = line size = 2w words or bytes
Number of blocks in main memory = 2s+ w/2w = 2s
Number of lines in cache = m = 2r
Size of tag = (s – r) bits
Size of cache 2r+w words or bytes

## Slide 26: Direct Mapping Address Structure
Tag s-r
Line r
Word w
8
14
2
24 bit address
2 bit word identifier (4 byte block)
22 bit block identifier
  8 bit tag (=22-14)
  14 bit line number
No two blocks in the same line have the same Tag field
Check contents of cache by finding line and checking Tag

## Slide 27: Direct-Mapping Cache Organization

## Slide 28: Direct-Mapping Cache Working
The cache system is presented with a 24-bit address
The 14-bit line number is used as an index into the cache to access a particular line
If the 8-bit tag number matches the tag number currently stored in that line, then the 2-bit word number is used to select one of the 4 bytes in that line
Otherwise, the 22-bit tag-plus-line field is used to fetch a block from main memory

## Slide 29: Direct Mapped Cache
Eight words in the cache
32 words in memory
An address X maps to the
direct-mapped cache word
X modulo 8

## Slide 30: Tags and Valid Bits
How do we know which particular block is stored in a cache location?
  Store block address as well as the data
  Actually, only need the high-order bits
  Called the tag
What if there is no valid data in a location?
  When a processor starts up, the cache does not have good data
  Valid bit: 1 = data is valid, 0 = data is invalid
  Initially 0

## Slide 31: Cache Example (Direct Mapped)
MM Size = 32B, MM addr(bits) = 5,1W = 1B
Block Size = 1B
nBlks in MM = MM Sz /Blk Sz = 32/1 = 32 Blks
Cache Size = 8B, nBlk in C = Cache Sizez/Block Size = 8/1 = 8 Blk
Index (line no) | V | Tag | Data
000 | N |  | 
001 | N |  | 
010 | N |  | 
011 | N |  | 
100 | N |  | 
101 | N |  | 
110 | N |  | 
111 | N |  | 

## Slide 32: Cache Example
Index (line no) | V | Tag | Data (1Bllk = 1 W = 1 Byte)
000 | N |  | 
001 | N |  | 
010 | N |  | 
011 | N |  | 
100 | N |  | 
101 | N |  | 
110 | Y | 10 | Mem[10110]
111 | N |  | 
MM Blk/Word addr (5bits) | Binary addr | Hit/miss | Cache block = (mm blk add % nBlk in C)
22 | 10 110 | Miss | (22%8=6) 110

## Slide 33: Cache Example
Index | V | Tag | Data
000 | N |  | 
001 | N |  | 
010 | Y | 11 | Mem[11010]
011 | N |  | 
100 | N |  | 
101 | N |  | 
110 | Y | 10 | Mem[10110]
111 | N |  | 
Word addr | Binary addr | Hit/miss | Cache block
26 | 11 010 | Miss | (26 mod 8 = 2) 010

## Slide 34: Cache Example
Index | V | Tag | Data
000 | N |  | 
001 | N |  | 
010 | Y | 11 | Mem[11010]
011 | N |  | 
100 | N |  | 
101 | N |  | 
110 | Y | 10 | Mem[10110]
111 | N |  | 
Word addr | Binary addr | Hit/miss | Cache block
22 | 10 110 | Hit | (22 mod 8 = ) 110
26 | 11 010 | Hit | (26 mod 8 = 2) 010

## Slide 35: Cache Example
Index | V | Tag | Data
000 | Y | 10 | Mem[10000]
001 | N |  | 
010 | Y | 11 | Mem[11010]
011 | Y | 00 | Mem[00011]
100 | N |  | 
101 | N |  | 
110 | Y | 10 | Mem[10110]
111 | N |  | 
Word addr | Binary addr | Hit/miss | Cache block
16 | 10 000 | Miss | (6 mod 8 = 0) 000
3 | 00 011 | Miss | (3 mod 8 = 3) 011
16 | 10 000 | Hit | (16 mod 8 = 0) 000

## Slide 36: Cache Example
Index | V | Tag | Data
000 | Y | 10 | Mem[10000]
001 | N |  | 
010 | Y | 10 | Mem[10010]
011 | Y | 00 | Mem[00011]
100 | N |  | 
101 | N |  | 
110 | Y | 10 | Mem[10110]
111 | N |  | 
Word addr | Binary addr | Hit/miss | Cache block
18 | 10 010 | Miss | (18 mod 8 = 2) 010

## Slide 37: Address Subdivision

## Slide 38: Address Subdivision - Example
Main Memory Size = 4GB
Main Memory address = 32 bits
Block Size = 1 word
1 Word = 4 Bytes => nbits for Byte offset = 2
Cache Memory Size = 4KB
No. of Cache Blocks = Cache Memory Size / Block Size (in Bytes)
= 4KB /4
= 1024 Blocks => 10 bits for line no
So no. of bits for Tag
= Main Memory address – (bits for Cache Block + bits for byte offset)
= 32 – (20 + 2) = 20

## Slide 39
The total number of bits in a direct-mapped cache is
2n × (block size + tag size + valid field size).

## Slide 40: Bits in a Cache
How many total bits are required for a direct-mapped cache with 16 KB of data and 4-word blocks, assuming a 32-bit address?
Each block has 4 * 32 or 128 bits of data plus a tag, which is 32 –( 10 + 2 + 2) bits, plus a valid bit
Thus, the total cache size is
210 *(4 * 32 + (32 - 10 - 2 - 2) + 1) = 210 * 147 bits = 18.4 KB

## Slide 41: Mapping an Address to a Multiword Cache Block
The address of the block is

## Slide 42: Mapping an Address to a Multiword Cache Block
Assume 32 bit address
Cache with 64 blocks and a block size of 16 bytes
  To what block number does address 1200 map?
Block address = 1200/16 = 75
Block number = 75 modulo 64 = 11
Tag
Index
Offset
0
3
4
9
10
31
4 bits
6 bits
22 bits

## Slide 43: Block Size Considerations
Larger blocks should reduce miss rate
  Due to spatial locality
But in a fixed-sized cache
  Larger blocks  fewer of them in cache
    More competition  increased miss rate
Larger blocks means large miss penalty as transfer time increases

## Slide 44: Cache Misses
On cache hit, CPU proceeds normally
On cache miss
  Stall the CPU pipeline
  Fetch block from next level of hierarchy
  Instruction cache miss or Data cache miss

## Slide 45
  Instruction cache miss

## Slide 46
Data cache miss
  Stall pipeline
  Send the address of data to memory
  Instruct main memory to perform a read and wait for the memory to complete its data access
  Write the cache entry, putting the data from memory in the data portion of the entry, writing the upper bits of the address (from the ALU) into the tag field, and turning the valid bit on
  Restart execution of instruction

## Slide 47: Write-Through
On data-write hit, could just update the block in cache
  But then cache and memory would be inconsistent
Write through: also update memory
But makes writes take longer
Solution: write buffer
  Holds data waiting to be written to memory
  CPU continues immediately
    Only stalls on write if write buffer is already full

## Slide 48: Write-Back
Alternative: On data-write hit, just update the block in cache
  Keep track of whether each block is dirty
When a dirty block is replaced
  Write it back to memory

## Slide 49: Associative Caches
Fully associative
  Allow a given block to go in any cache entry
  Requires all entries to be searched at once
  Comparator per entry (expensive)
n-way set associative
  Each set contains n entries
  Block number determines which set
    (Block number) modulo (#Sets in cache)
  Search all entries in a given set at once
  n comparators (less expensive)

## Slide 50: Associative Cache Example

## Slide 51: Spectrum of Associativity
For a cache with 8 entries

## Slide 52: Associativity Example
Compare 4-block caches
  Direct mapped, 2-way set associative, fully associative
  Block access sequence: 0, 8, 0, 6, 8
Direct mapped
Block address | Cache index | Hit/miss | Cache content after access |  |  | 
 |  |  | 0 | 1 | 2 | 3
0 | 0 | miss | Mem[0] |  |  | 
8 | 0 | miss | Mem[8] |  |  | 
0 | 0 | miss | Mem[0] |  |  | 
6 | 2 | miss | Mem[0] |  | Mem[6] | 
8 | 0 | miss | Mem[8] |  | Mem[6] | 

## Slide 53: Associativity Example
2-way set associative
Block address | Cache index | Hit/miss | Cache content after access |  |  | 
 |  |  | Set 0 |  | Set 1 | 
0 | 0 | miss | Mem[0] |  |  | 
8 | 0 | miss | Mem[0] | Mem[8] |  | 
0 | 0 | hit | Mem[0] | Mem[8] |  | 
6 | 0 | miss | Mem[0] | Mem[6] |  | 
8 | 0 | miss | Mem[8] | Mem[6] |  | 
Fully associative
Block address |  | Hit/miss | Cache content after access |  |  | 
0 |  | miss | Mem[0] |  |  | 
8 |  | miss | Mem[0] | Mem[8] |  | 
0 |  | hit | Mem[0] | Mem[8] |  | 
6 |  | miss | Mem[0] | Mem[8] | Mem[6] | 
8 |  | hit | Mem[0] | Mem[8] | Mem[6] | 

## Slide 54: Set Associative Cache Organization

## Slide 55: Replacement Policy
Direct mapped: no choice
Set associative
  Prefer non-valid entry, if there is one
  Otherwise, choose among entries in the set
Least-recently used (LRU)
  Choose the one unused for the longest time
    Simple for 2-way, manageable for 4-way, too hard beyond that
Random
  Gives approximately the same performance as LRU for high associativity