## Slide 1: BITS Pilani
Department of Computer Science

## Slide 2
Data Link Layer

## Slide 3: Multiple Access Mechanisms

## Slide 4: Random Access Protocols
In random access or contention methods, no station is superior to another station and none is assigned then control over another. No station permits another station to send.
At each instance, a station that has data to send uses a procedure defined by the protocol to make a decision on whether or not to send.

## Slide 5: Random Access Protocols
when node has packet to send
  transmit at full channel data rate
  not a priori coordination among nodes
>= 2 nodes transmit concurrently ➜ “collision”
random access MAC protocol specification
  collision detection
  collision recovery
types
  Pure ALOHA, slotted ALOHA
  CSMA, CSMA/CD, CSMA/CA

## Slide 6: key ideas of random access
station model
  n independent stations (nodes, terminals)
single channel
  all transmission/reception on shared channel
  nodes have equivalent ability
time
  continuous
  slotted (discrete, timed intervals, “master clock”)

## Slide 7: key ideas of random access
carrier sense (or not)
  listen before speaking, and don’t interrupt
  check if someone else is already sending data ...
  … wait till the other node is done
collision detection (or not)
  if someone else starts talking at the same time, stop
  if the data on the wire is garbled ...
  ... another node is transmitting, too, so stop
randomness
  don’t start talking again right away
  wait for a random time before trying again

## Slide 8: ALOHA Network

## Slide 9: Frames in Pure ALOHA

## Slide 10: ALOHA Protocol

## Slide 11: ALOHA: Vulnerable Time

## Slide 12: ALOHA: Throughput
Assume number of stations trying to transmit follow Poisson Distribution
The throughput for pure ALOHA is
S = G × e−2G
where G is the average number of frames requested per frame-time
The maximum throughput
  Smax = 0.184 when G= 1/2
  The number of packets successfully transmitted through the channel per packet time.

## Slide 13: Slotted ALOHA
assumptions
all frames same size
time divided into equal slots (time to transmit a frame)
nodes start to transmit frames only at start of slots
nodes are synchronized
if two or more nodes transmit, all nodes detect collision
operation
when node obtains fresh frame, transmits in next slot
no collision: node can send new frame in next slot
collision: node retransmits frame in each subsequent slot with probability p until success

## Slide 14: Slotted ALOHA

## Slide 15: Slotted ALOHA: Vulnerable Time

## Slide 16: Slotted ALOHA: Throughput
The throughput for Slotted ALOHA is
S = G × e−G
where G is the average number of frames requested per frame-time
The maximum throughput
  Smax = 0.368 when G= 1

## Slide 17: Pure vs. Slotted ALOHA
Throughput versus offered traffic for ALOHA systems.
max throughput: ALOHA 1/(2e) ~ 18%; slotted ALOHA 1/e ~ 37%

## Slide 18: Carrier Sense Multiple Access (CSMA)
The capacity of ALOHA or slotted ALOHA is limited by the large vulnerability period of a packet.
By listening before transmitting, stations try to reduce the vulnerability period to one propagation delay.
This is the basis of CSMA (Kleinrock and Tobagi, UCLA, 1975)
Same assumptions made for ALOHA are made now for CSMA.

## Slide 19: Carrier Sense Multiple Access (CSMA)
Invented to minimize collisions and increase the performance
A station now “follows” the activity of other stations
Simple rules for a polite human conversation
  Listen before talking
  If someone else begins talking at the same time as you, stop talking
CSMA:
A node should not send if another node is already sending → carrier sensing
CD (collision detection):
A node should stop transmission if there is interference → collision detection

## Slide 20: Assumptions with CSMA Networks
1. Constant length packets
2. No errors, except those caused by collisions
3. Each host can sense the transmissions of all other hosts
4. The propagation delay is small compared to the transmission time

## Slide 21: Collision in CSMA
B
C

## Slide 22: CSMA: Vulnerable Time

## Slide 23: Persistence Methods
What a station does when channel is idle or busy
There are several types of CSMA protocols:
1-Persistent CSMA
Non-Persistent CSMA
P-Persistent CSMA

## Slide 24: 1-Persistence Methods
Sense the channel.
  – If busy, keep listening to the channel and transmit immediately when the channel becomes idle.
  – If idle, transmit a packet immediately.
If collision occurs,
  – Wait a random amount of time and start over again.

## Slide 25: Non-Persistence Methods
• Sense the channel.
  – If busy, wait a random amount of time and sense the channel again
  – If idle, transmit a packet immediately
If collision occurs
  – wait a random amount of time and start all over again
Notes: The protocol is called 1-persistent because
the host transmits with a probability of 1
whenever it finds the channel idle.

## Slide 26: P-Persistence Methods
• Optimal strategy: use P-Persistent CSMA
• Assume channels are slotted
• One slot = contention period (i.e., one round trip propagation delay)
• This method is used when channel has time slots such that the time slot duration is equal to or greater than the maximum propagation delay time.
Notes: The protocol is called 1-persistent because
the host transmits with a probability of 1
whenever it finds the channel idle.

## Slide 27: P-Persistence Methods
• Whenever a station becomes ready to send, it senses the channel.
• If channel is busy, station waits until next slot.
• If channel is idle, it transmits with a probability p.
• With the probability q=l-p, the station then waits for the beginning of the next time slot.
• If the next slot is also idle, it either transmits or waits again with probabilities p and q.
• This process is repeated till either frame has been transmitted or another station has begun transmitting.
• In case of the transmission by another station, the station acts as though a collision has occurred and it waits a random amount of time and starts again.
Notes: The protocol is called 1-persistent because
the host transmits with a probability of 1
whenever it finds the channel idle.

## Slide 28: Persistence Methods

## Slide 29: CSMA/CD Protocol
CSMA improves on the performance of ALOHA tremendously.
The remaining limitation is that, once a packet is sent, feedback occurs a roundtrip time after the entire packet is transmitted.
The solution to improve on the performance of CSMA is to listen to the channel while a packet is being sent.
This is called collision detection.

## Slide 30: CSMA/CD Protocol
All hosts transmit & receive on one channel
Packets are of variable size.
When a host has a packet to transmit:
1. Carrier Sense: Check that the line is quiet before transmitting.
2. Collision Detection: Detect collision as soon as possible. If a collision is detected, stop transmitting; wait a random time, then return to step 1.
binary exponential backoff

## Slide 32: CSMA/CD

## Slide 33: CSMA/CD Network Size Restriction
To ensure that a packet is transmitted without a collision, a host must be able to detect a collision before it finishes transmitting a packet.
PROP
PROP
t=0
t=PROP--
t=PROP
t=2PROP-
A
B
Events:
t=0: Host A starts transmitting a packet.
t=PROP--: Just before the first bit reaches Host B, Host B senses the line to be idle and starts to transmit a packet.
t=PROP-: A collision takes place near Host B.
t=PROP: Host B receives data whilst transmitting, and so detects the collision. t=2PROP-: Host A receives data whilst transmitting, and so detects the collision.
“Line is idle”
t=PROP-
“Line is idle”

## Slide 34: CSMA/CD Network Size Restriction
“To ensure that a packet is transmitted without a collision, a host must be able to detect a collision before it finishes transmitting a packet.”

## Slide 35: CSMA/CD: Flow Diagram

## Slide 37: Energy Levels

## Slide 38: CSMA/CA
Energy level method may not suitable for wireless medium since the lost of energy in wireless transmission.
CSMA/CD is not possible in wireless.
CSMA/CA Used in a network where collision cannot be detected. E.g., wireless LAN.
IFS – Interframe Space

## Slide 39: Distributed Coordination Function
DCF sublayer uses CSMA
  if station has frame to send it listens to medium
  if medium idle, station may transmit
  else waits until current transmission complete
No collision detection since on wireless network
DCF includes delays that act as a priority scheme

## Slide 40: DCF Basic mode

## Slide 41: CSMA/CA: Flow Diagram

## Slide 42: CSMA/CA
CSMA protocols sense the carrier, but sensing the carrier does not always releases true information about the status of the wireless channel
    There are two problems that are unique to wireless channels (different than wireline channels), that makes CSMA useless in some cases. These problems are:
        Hidden terminal problem
        Exposed terminal problem.

## Slide 43: Collision Avoidance Mechanisms
Problem:
  Two nodes, hidden from each other, transmit complete frames to base station
  Wasted bandwidth for long duration!
Solution:
  Small reservation packets: RTS+CTS
  Nodes track reservation interval with internal “network allocation vector” (NAV)

## Slide 44: Hidden Terminal Problem
B
C
A
A is transmitting to B.
C is sensing the carrier and detects that it is idle (It can not hear A’s transmission).
C also transmits and collision occurs at B.
A is hidden from C.
A’s cell
C’s cell
Hidden
terminal

## Slide 45: Exposed Terminal Problem
B
C
A
B’s cell
C’s cell
D
B is transmitting to A. C is hearing this transmission.
C now wants to transmit to D. It senses the existence of carrier signal and
defers transmission to D.
However, C can actually start transmitting to D while B is transmitting to A,
Since A is out of range of C and C’s signals can not be heard at A.
C is exposed to B’s transmission.
Exposed
terminal

## Slide 46: Solution Concept
Y, I want to talk to you!
Y, I want to talk to you!
X, lets talk! I am available.
X
Z
Y

## Slide 47: Multiple Access with Collision Avoidance (MACA) Protocol
When a station wants to transmit data
    It sends an RTS (Ready-to-Send) packet to the intended receiver
        The RTS packet contains the length of the data that needs to be transmitted
        Any station other than the intended recipient hearing RTS defers transmission for a time duration equal to the end of the corresponding CTS reception
    The receiver sends back CTS (Clear-to-Send) packet back to sender if it is available to receive.
        The CTS packet contains the length of the data that original sender wants to transmit
        Any station other than the original RTS sender, hearing CTS defers transmission until the data is sent.
    The original sender upon reception of the CTS, starts transmitting.

## Slide 48: DCF + RTS/CTS

## Slide 49: CSMA/CA and NAV
Distributed coordination function (DCF) Inter frame sequence (DIFS)
Short Inter frame sequence (SIFS)
Notes: Distributed coordination function (DCF) Inter frame sequence (DIFS)

## Slide 50: MACA Solution for Hidden Terminal Problem
B
C
A
A’s cell
C’s cell
CTS(n)
Data(n)
CTS(n)
X
RTS(n)
RTS(n)
C defers transmission
for duration of n bytes of
data transmission. Node A
is no longer hidden from C effectively.
X defers transmission
until expected CTS
reception time by RTS
sender.
A is transmitting to B.

## Slide 51: MACA Solution for Exposed Terminal Problem
B
C
A
B’s cell
C’s cell
D
B is transmitting to A
RTS(n)
CTS(n)
RTS(n)
Data(n)
C defers transmission upon hearing B’s RTS until B could get CTS from A.
After that C can start transmission to D. For that it first sends an RTS.
C is not longer exposed to the data transmission of B.
CTS

## Slide 52
Reservation access method
Stations take turns transmitting a single frame at a full rate ( R ) bps
Transmissions are organized into variable length cycles
Each cycle begins with a reservation interval that consists of (N) minislots. One minislot for each of the N stations
When a station needs to send a data frame, it makes a reservation in its own minislot.
By listening to the reservation interval, every station knows which stations will transfer frames, and in which order.
The stations that made reservations can send their data frames after the reservation frame.

## Slide 53: Polling
Stations take turns accessing the medium
Two models: Centralized and distributed polling
Centralized polling
  One device is assigned as primary station and the others as secondary stations
  All data exchanges are done through the primary
  When the primary has a frame to send it sends a select frame that includes the address of the intended secondary
  When the primary is ready to receive data it send a Poll frame for each device to ask if it has data to send or not. If yes, data will be transmitted otherwise NAK is sent.
  Polling can be done in order (Round-Robin) or based on predetermined order
Distributed polling
  No primary and secondary
  Stations have a known polling order list which is made based on some protocol
  station with the highest priority will have the access right first, then it passes the access right to the next station (it will send a pulling message to the next station in the pulling list), which will passes the access right to the following next station, …

## Slide 54
Select and poll functions in polling access method
Primary is sending to Secondary
Secondary is sending to Primary

## Slide 55
Token-Passing network
Station Interface is in two states:
  Listen state: Listen to the arriving bits and check the destination address to see if it is its own address. If yes the frame is copied to the station otherwise it is passed through the output port to the next station.
  Transmit state: station captures a special frame called free token and transmits its frames. Sending station is responsible for reinserting the free token into the ring medium and for removing the transmitted frame from the medium.
listen mode
1 bit delay
transmit mode
delay
to station
from station
input
from
ring
output
to
ring
to station
from station
Implements Distributed Polling System
Bits are inserted by the station
bits are copied to the output bits with a one bit delay

## Slide 56
Token-passing procedure

## Slide 59
Suppose nodes A and B are on the same 10Mbps Ethernet segment and them propagation delay between the two nodes is 225 bit times. Suppose A and B send frames at the same time, the frames collide, and then A and B choose different values of K in the CSMA/CD algorithm. Assuming no other nodes are active, can the retransmissions from A and B collide? For our purposes, it suffices to work out the following example. Suppose A and B begin transmission at t=0 bit times. They both detect collisions at t=225 bit times. They finish transmitting a jam signal at t=225+48=273 bit times Suppose K_a=0 and K_b=1. At what time does B schedule its retransmission? At what time does A begin transmission?