## Slide 1: Network Simulator-2 (Part 1)
Dr. Pranav M. Pawar

## Slide 2
Object Oriented simulator
Work at packet level
Widely used in research community
Use two languages
  TCL
  C++
Ns-2 Installation
  Refer to Appendix
Introduction to NS-2

## Slide 3
Simulation System Architecture
Trace files (.tr)
----------------
----------------
Animation File (.nam)
----------------
----------------
----------------
----------------
Otcl Script
----------------
----------------
----------------
----------------
Simulation Results
Otcl : TCL Interpreter with OO Extension
NS Simulator Library
NS-2 Shell

## Slide 4
Save the simulation script in specific folder.
Open the terminal and go up to specific folder.
Run the simulation script,
  ns: command to run simulation script.
    Syntax: ns filename.tcl
      e.g. ns First_script_wired.tcl
Run the nam file,
  nam: command to run animation file
    Syntax: nam filename.nam
      e.g. nam s1.nam
Running the Simulation Script

## Slide 5
Simulation Scenario
0
1
5
4
3
2
2 Mb, 10ms
2 Mb, 10ms
0.5 Mb, 40ms
0.5 Mb, 30ms
0.3 Mb, 100ms
TCP
Null
TCPSink
UDP
CBR
FTP

## Slide 6
#Create Simulator Object (Simulator is class in ns2)
set ns [new Simulator]
#Define different colors for data flows (for NAM) ($ means reference)
$ns color 1 Blue
$ns color 2 Red
#Open the Event trace files
set file1 [open out.tr w]
#trace-all for capturing event trace.
$ns trace-all $file1
#Open the NAM trace file
set file2 [open out.nam w]
#namtrace-all for capturing animation details.
$ns namtrace-all $file2
Simulation Script

## Slide 7
#Create six nodes
set n0 [$ns node]
set n1 [$ns node]
set n2 [$ns node]
set n3 [$ns node]
set n4 [$ns node]
set n5 [$ns node]
#Create links between the nodes
#Syntax: $ns duplex-link source destination data-rate propagation-delay queue-type
#DropTail class for simple queue.
  $ns duplex-link $n0 $n2 2Mb 10ms DropTail
  $ns duplex-link $n1 $n2 2Mb 10ms DropTail
  $ns simplex-link $n2 $n3 0.3Mb 100ms DropTail
  $ns simplex-link $n3 $n2 0.3Mb 100ms DropTail
  $ns duplex-link $n3 $n4 0.5Mb 40ms DropTail
  $ns duplex-link $n3 $n5 0.5Mb 30ms DropTail
Simulation Script (contd..)

## Slide 8
#Give node position (for NAM)
#Syntax: $ns duplex-link-op source destination orient orientation-position
  $ns duplex-link-op $n0 $n2 orient right-down
  $ns duplex-link-op $n1 $n2 orient right-up
  $ns simplex-link-op $n2 $n3 orient right
  $ns simplex-link-op $n3 $n2 orient left
  $ns duplex-link-op $n3 $n4 orient right-up
  $ns duplex-link-op $n3 $n5 orient right-down
Simulation Script (contd..)
Node
Up
Down
Left-Down
Right-Down
Right-Up
Left-Up
Right
Left

## Slide 9
#Set Queue Size of link (n2-n3) to 40
#Syntax: $ns queue-limt source destination queue-size
  $ns queue-limit $n2 $n3 40
#Setup a TCP connection (Source agent: TCP, Destination agent: TCPSink)
#Agent is superclass and TCP is subclass.
set tcp [new Agent/TCP]
$ns attach-agent $n0 $tcp
#Agent is superclass and TCPSink is subclass.
set sink [new Agent/TCPSink]
$ns attach-agent $n4 $sink
$ns connect $tcp $sink
$tcp set fid_ 1
$tcp set packetSize_ 552
#Setup a FTP over TCP connection
#Application is superclass and FTP is subclass.
set ftp [new Application/FTP]
$ftp attach-agent $tcp
Simulation Script (contd..)

## Slide 10
#Setup a UDP connection (Source agent: UDP, Destination agent: Null)
#Agent is superclass and UDP is subclass.
set udp [new Agent/UDP]
$ns attach-agent $n1 $udp
#Agent is superclass and Null is subclass.
set null [new Agent/Null]
$ns attach-agent $n5 $null
$ns connect $udp $null
$udp set fid_ 2
#Setup a CBR over UDP connection
#CBR(Constant Bit Rate) is subclass of Traffic and Traffic is subclass of Application
set cbr [new Application/Traffic/CBR]
$cbr attach-agent $udp
$cbr set packet_size_ 1000
Simulation Script (contd..)

## Slide 11
# Scheduling the event
  $ns at 0.1 "$cbr start"
  $ns at 1.0 "$ftp start"
  $ns at 624.0 "$ftp stop"
  $ns at 624.5 "$cbr stop“
  # Call finish procedure
  $ns at 625.0 “finish”
# Run the simulation
  $ns run
Simulation Script (contd..)
#Define a 'finish' procedure
proc finish {} {
global ns file1 file2
$ns flush-trace
close $file1
close $file2
exit 0 }

## Slide 12
Wired trace file format
Event | Time | From-Node | To-Node | Pkt-Type | Pkt-Size | Flags | Fid | Src-addr | Dest-addr | Seq-num | Pkt-id
- | 1.06 | 0 | 2 | tcp | 1040 | ------- | 1 | 0.0 | 3.0 | 2 | 124
r | 1.07 | 1 | 2 | cbr | 1000 | ------- | 2 | 1.0 | 3.1 | 120 | 122
+ | 1.07 | 2 | 3 | cbr | 1000 | ------- | 2 | 1.0 | 3.1 | 120 | 122
d | 1.07 | 2 | 3 | cbr | 1000 | ------- | 2 | 1.0 | 3.1 | 120 | 122

## Slide 13
Self Practice Example
1
3
7
6
5
4
2 Mb, 10ms
2 Mb, 10ms
0.5 Mb, 40ms
0.5 Mb, 30ms
0.3 Mb, 100ms
TCP
Null
TCPSink
UDP
CBR
FTP
9
8
0
2 Mb, 10ms
2 Mb, 10ms
0.5 Mb, 30ms
0.5 Mb, 30ms
2

## Slide 14
Steps for making your machine ready for NS-2
  Install Ubuntu Linux on your machine (As dual boot system ot Using Vmware/Virtual Box).
    Steps for installing ubuntu (recommended version: Ubuntu 20.04.2):
https://itsfoss.com/install-linux-in-virtualbox
  Login (using user name and password which you selected during installation) to Ubuntu Linux
  Open terminal (Right click on desktop screen and select open terminal).
  NS-2 installation
    Type following command on terminal and follow instructions
      sudo apt-get install ns2
    Install nam
      sudo apt-get install nam
Appendix

## Slide 15
https://www.isi.edu/nsnam/ns/tutorial/
https://www.geeksforgeeks.org/basics-of-ns2-and-otcltcl-script/
https://www.isi.edu/nsnam/ns/
Steps for installing ubuntu (recommended version: Ubuntu 20.04.2):
https://itsfoss.com/install-linux-in-virtualbox/
Sources

## Slide 16
Thank You!